## Slide 1: Fundamentals of IoT Software © 2021 by Luca Mottola is licensed under CC BY-NC 4.0 To view a copy of this license, visit creativecommons.org/licenses/by-nc/4.0/

## Slide 2: Fundamentals of IoT Software MQTT Luca Mottola luca.mottola@polimi.it (version 0.1)

## Slide 3: RPL Border Router
We need a “man-in-the-middle” bridging the IoT network with the external Internet
In Contiki-NG: examples/rpl-border-router
  Configured to also become the root of the RPL tree

## Slide 4
Notes: DIRECTIONS FOR INSTRUCTORS
In COOJA (check cheat sheet to setup the RPL border router):
Create a simulation with examples/rpl-border-router and multiple examples/hello-world nodes, once it’s up and running
Ping6 of the border router IPv6 from the VM terminal
Add more examples/hello-world nodes
Show you can ping6 any other node, going through the RPL tree

## Slide 5: Complete Stack Configuration

## Slide 6: MQTT Overview
An extremely lightweight Pub/Sub messaging layer
  Decoupling and asynchronous group communication!
Payload agnostic
Topic-based
  Topics are arranged hierarchically
  Examples:
    iot
    iot/building21
    iot/building21/temperature
  Effectively represent nested “channels”

## Slide 7: MQTT QoS
MQTT QoS is a per-message agreement on the guarantees on delivery
QoS0: at most once
QoS1: at least once
QoS2: at most once

## Slide 8: MQTT Persistent Sessions
Normal behavior:
  Clients subscribe upon connecting to the broker
  Subscriptions are lost when disconnecting
Persistent sessions save the subscriptions of clients as they go off-line
If so, the MQTT broker queues all QoS1 and QoS2 messages published while that client was off-line
The client automatically re-send unconfirmed QoS1 and QoS2 published messages
Careful: may backfire if the client is long disconnected

## Slide 9: MQTT in Contiki-NG
Implementation compliant with v.3.1
Does not support QoS2
Contiki-NG devices can operate as publisher, subscriber, or both

## Slide 10: MQTT: API (part 1)
typedef void (*mqtt_event_callback_t)(struct mqtt_connection *m,
mqtt_event_t event,
void *data);
mqtt_status_t mqtt_register(struct mqtt_connection *conn,
struct process *app_process,
char *client_id,
mqtt_event_callback_t event_callback,
uint16_t max_segment_size);
Notify of important MQTT events, such as connection open, acknowledgement after publish if using QoS1, …
Setup the connection to the MQTT broker

## Slide 11: MQTT: API (part 2)
mqtt_status_t mqtt_connect(struct mqtt_connection *conn,
char *host,
uint16_t port,
uint16_t keep_alive);
mqtt_status_t mqtt_subscribe(struct mqtt_connection *conn,
uint16_t *mid,
char *topic,
mqtt_qos_level_t qos_level);
mqtt_status_t mqtt_publish(struct mqtt_connection *conn,
uint16_t *mid,
char *topic,
uint8_t *payload,
uint32_t payload_size,
mqtt_qos_level_t qos_level,
mqtt_retain_t retain);
Establish the connection to the broker
Subscribe to a topic
Publish a message

## Slide 12: MQTT: Example (1)
Lives in examples/mqtt-demo
Connects to an MQTT broker running at fd00::1
Periodically publishes messages to iot/native/launchpad/json
Subscribes to iot/native/launchpad/json
Published messages include meta-data and a fake temperature reading

## Slide 13: MQTT: Example (2)
If you are bridging to mqtt.neslab.it…
Notes: NOTE TO INSTRUCTORS: the Contiki-NG cheat sheet includes instructions to bridge mosquitto on the VMs to a public MQTT server that can be used in any other app..

## Slide 14
Notes: DIRECTIONS FOR INSTRUCTORS:
Using COOJA or CC260/CC1350 nodes:
Setup a RPL network using examples/rpl-border-router
Deploy one or two examples/mqtt-demo nodes
Show MQTT messages arriving at mosquitto on the VM
If bridging, show messages being published on the Internet… and the chain is complete!

## Slide 15: Exercise 6
Modify the mqtt-demo example so that a different message is published on a different topic depending on the outcome of a random number