## Slide 1: Fundamentals of IoT Software © 2021 by Luca Mottola is licensed under CC BY-NC 4.0 To view a copy of this license, visit creativecommons.org/licenses/by-nc/4.0/

## Slide 2: Fundamentals of IoT Software Energy Management Luca Mottola luca.mottola@polimi.it (version 0.1)

## Slide 3: Radio Duty-cycling

## Slide 4: Radio Duty-cycling for Dummies
In a nutshell..
  Turn on when you need it
  Turn it off when you don’t
In Contiki-NG
  #include “netstack.h”
  NETSTACK_RADIO.on();
  NETSTACK_RADIO.off();
Simple, isn’t it?

## Slide 5
Notes: DIRECTIONS TO INSTRUCTORS:
- Modify examples/blink.c to switch the radio on or off as it blinks, run in COOJA with SKY motes and observe the timeline!

## Slide 6: Exercise 7
Modify the rpl-upd example so you try and turn off the radio as much as possible
Start in COOJA, then verify your design on hardware
Notes: NOTE TO INSTRUCTORS:
- Duty cycling done manually here is going to mess up RPL.. This is intentional as it introduces the proper duty-cycling.

## Slide 7: Problem(s)
How do you know when you need to transmit?
  Application demands, system constraints, …
How do you know when you are supposed to receive?
  May not know what other devices are doing…
An entire application and network stack on top of the radio
  Want to minimize disruption
  Transparent operation would be ideal

## Slide 9: Duty-cycling in MACs (1)
Asynchronous, sender-initiated
  X-MAC, ContikiMAC, …
Asynchronous, receiver-initiated
  RI-MAC, A-MAC, …
Burden on the sender…
Burden on the receiver…

## Slide 10: Duty-cycling in MACs (2)
Synchronous
  T-MAC, TSCH, …
Everybody knows when to talk and when to listen

## Slide 11: Duty-cycling: Trade-offs
Sender-initiated
  Pro: no data, no traffic
  Cons: channel occupation when actually transmitting
Receiver-initiated
  Pro: channel occupation when transmitting
  Cons: higher-latency as probe intervals grow
Both asynchronous solutions handle topology changes with no reconfiguration
Synchronous:
  Pro: minimal radio-on time
  Pro: predictable latency
  Pro: bandwidth reservation
  Cons: topology changes require reconfiguring the schedule
Sender-initiated
Synchronous
Receiver-initiated

## Slide 12: TSCH in Contiki-NG
TSCH is a channel-hopping time-slotted MAC protocol part of 802.15.4
6TiSCH customizes TSCH to run IPv6 over RPL
Contiki-NG includes an implementation of 6TiSCH and TSCH able to run transparently below RPL
  To enable it include MAKE_MAC = MAKE_MAC_TSCH in the Makefile
  Shell commands are available too: tsch-set-coordinator and tsch-status

## Slide 13
Notes: DIRECTIONS FOR INSTRUCTORS:
Check the execution of examples/rpl-udp with TSCH in COOJA, using COOJA motes.. Look at the timeline!
Using hardware, the instructor runs the rpl border router, others use examples/blink-shell with TSCH to check the shell commands

## Slide 14: Energy Metering

## Slide 15: Energy Metering
How do I finally know how how much energy are the different components consuming?

## Slide 16: Contiki-NG Energest
Contiki-NG includes a lightweight software-only tool called Energest
It tracks the amount of time the different components spend in various states
Given the times, a little digging in the datasheet, and you know the energy!
Enable Energest with #define ENERGEST_CONF_ON 1 in your project-conf.h

## Slide 17: Energest Example: Radio
It tells you that in 120 seconds of execution, your radio was
  20 seconds in LISTEN state
  10 seconds in TRANSMIT state
  90 seconds in OFF state
The datasheet of your imaginary device says
  10 mA in LISTEN
  8 mA in TRANSMIT
  20uA in OFF
Your device is powered by a pair of AA batteries
  We consider constant 3V as a first (over)approximation
The energy consumed by your radio in the first 120 seconds of execution therefore is upper-bound by:
  E = C x V x t
  3V x ((10 mA x 20 s) + (8mA x 10 s) + (20uA x 90 s))
  0.6 J + 0.24 J +0.0054 J = 0,8454 J

## Slide 18: Energest Example Code
#include “sys/energest.h”
PROCESS_THREAD(energest, ev, data)
{
static struct etimer et;
PROCESS_BEGIN();
etimer_set(&et, CLOCK_SECOND * 20);
while(1) {
PROCESS_WAIT_EVENT_UNTIL(etimer_expired(&et));
etimer_reset(&et);
energest_flush();
printf("Energest CPU: Active %lu LPM: %lu Deep LPM: %lu Total time: %lu seconds\n",
(unsigned long)(energest_type_time(ENERGEST_TYPE_CPU) / ENERGEST_SECOND),
(unsigned long)(energest_type_time(ENERGEST_TYPE_LPM) / ENERGEST_SECOND),
(unsigned long)(energest_type_time(ENERGEST_TYPE_DEEP_LPM) / ENERGEST_SECOND),
(unsigned long)(ENERGEST_GET_TOTAL_TIME() / ENERGEST_SECOND));
printf("Energest Radio: Listen: %lu Transmit: %lu seconds\n",
(unsigned long)(energest_type_time(ENERGEST_TYPE_LISTEN) / ENERGEST_SECOND),
(unsigned long)(energest_type_time(ENERGEST_TYPE_TRANSMIT) / ENERGEST_SECOND));
}
PROCESS_END();
}
Required to force Energest to update all counters
Print the current values in seconds

## Slide 19
Notes: DIRECTIONS TO INSTRUCTORS:
- Using Sky or COOJA motes, check the execution of examples/blink-energest in COOJA

## Slide 20: Exercise 8
Modify your hand-crafted duty-cycle solution of Exercie 7 to use Energest
Use Energest when running rpl-udp using TSCH
Compare the result.. who’s more energy efficient?