## Slide 1: Fundamentals of IoT Software © 2021 by Luca Mottola is licensed under CC BY-NC 4.0 To view a copy of this license, visit creativecommons.org/licenses/by-nc/4.0/

## Slide 2: Fundamentals of IoT Software Memory Handling Luca Mottola luca.mottola@polimi.it (version 0.1)

## Slide 3: Memory in Embedded Systems
Tend to employ static memory allocation
  Free from leaks and fragmentation
  Easier to debug
IoT software has dynamic memory requirements
  No over-allocation

## Slide 4: MEMB in Contiki-NG
Memory blocks are allocated in static memory
#define MEMB(name, structure, num)
void memb_init(struct memb *m);
void *memb_alloc(struct memb *m);
char memb_free(struct memb *m, void *ptr);
int memb_inmemb(struct memb *m, void *ptr);
int memb_numfree(struct memb *m);
Allocates a memory block with given name, for a given data structure, for a given number of instances

## Slide 5: MEMB Example
struct connection {
int socket;
};
MEMB(connections, struct connection, 16);
struct connection* open_connection(int socket)
{
struct connection *conn;
conn = memb_alloc(&connections);
if(conn == NULL) {
return NULL;
}
conn->socket = socket;
return conn;
}
void
close_connection(struct connection *conn)
{
memb_free(&connections, conn);
}
Maximum number of existing connections!

## Slide 6: Heap Memory in Contiki-NG
Standard malloc() and free() are available
  Not necessarily optimized for resource-constrained IoT devices
HeapMem has optimized fragmentation schemes
Semantics is the same as standard heap functionality
void *heapmem_alloc(size_t size);
void *heapmem_realloc(void *ptr, size_t size);
void heapmem_free(void *ptr);
void heapmem_stats(heapmem_stats_t *stats);

## Slide 7: Understanding Memory
Running size on the .elf file
  Code section: text
  Static non-initialized memory: bss
  Static initialized memory: data
  Total all together: dec
Profiling info are included in .ramprof and .flashprof
Notes: DIRECTIONS FOR INSTRUCTORS:
- Run make NAME.flashprof or NAME.ramprof to get stats, check the stack size in the latter

## Slide 8: Tuning Memory
Packets in the link-layer queue
Override configuration in project-conf.h !
Neighbor table size
Routing table entries
IPv6 packet buffer
6LowPAN packet fragmentation