## Slide 1: Fundamentals of IoT Software © 2021 by Luca Mottola is licensed under CC BY-NC 4.0 To view a copy of this license, visit creativecommons.org/licenses/by-nc/4.0/

## Slide 2: Fundamentals of IoT Software Mbed Timers and Threads Luca Mottola luca.mottola@polimi.it (version 0.1)

## Slide 3: How To Blink?
#include "mbed.h"
DigitalOut led(LED1);
int main()
{
while(1) {
led = 1;
wait(0.2);
led = 0;
wait(0.8);
}
}
In Mbed, wait is implemented using busy waits…
Peripherals are accessed via their Digital or Analog mapping
Notes: CODE PUBLISHED AT: https://os.mbed.com/users/lmottola/code/IOTSoftware-BlinkBusy/

## Slide 4: How To Blink Better…
#include "mbed.h"
Ticker toggle_led_ticker;
DigitalOut led1(LED1);
void toggle_led() {
led1 = !led1;
}
int main() {
toggle_led_ticker.attach(&toggle_led, 0.1);
while (true) {
// Do other things...
}
}
Ticker objects use Timer interrupts to periodically trigger an action
Functions given to tickers cannot have parameters!
Notes: CODE PUBLLISHED AT: https://os.mbed.com/users/lmottola/code/IOTSoftware-BlinkTicker/

## Slide 5: How To Blink Best!
#include "mbed.h"
DigitalOut led1(LED1);
DigitalOut led2(LED2);
Thread thread;
void led2_thread() {
while (true) {
led2 = !led2;
wait(1);
}
}
int main() {
thread.start(led2_thread);
while (true) {
led1 = !led1;
wait(0.5);
}
}
It’s a Thread object!
The thread executes concurrently with main!
Starts the thread by executing led2_thread
Notes: CODE PUBLISHED AT: https://os.mbed.com/users/lmottola/code/IOTSoftware-BlinkThread/

## Slide 6: How To Blink Best and Generic!
#include "mbed.h"
Thread thread;
DigitalOut led1(LED1);
volatile bool running = true;
void blink(DigitalOut *led) {
while (running) {
*led = !*led;
wait(1);
}
}
int main() {
thread.start(callback(blink, &led1));
wait(5);
running = false;
thread.join();
}
Blinks a generic LED once a second
Spawns a thread to blink LED1 for 5 seconds, then stops
It’s a Thread object!
When using synchronization variables, better be volatile!
Notes: CODE PUBLISHED AT: https://os.mbed.com/users/lmottola/code/IOTSoftware-BlinkThreadCallback/

## Slide 7
Notes: DIRECTIONS FOR INSTRUCTORS:
- Write the first Blink with busy waits from scratch; do not include mbed at first; import, compile, and deploy on the board.
- Proceed with the other three with importing.

## Slide 8: STDin and STDout
#include "mbed.h"
DigitalOut myled(LED1);
Serial pc(USBTX, USBRX);
int main() {
char buffer[128];
pc.printf("Starting..\n");
while (1) {
pc.gets(buffer, 4);
pc.printf("I got '%s'\n", buffer);
}
}
The built-in Serial class allows to use STDin and STDout through the USB connect!
Need terminal software to read and write form the USB serial line
Notes: CODE PUBLISHED AT: https://os.mbed.com/users/lmottola/code/IOTSoftware-STDinSTDout/

## Slide 9
Notes: DIRECTIONS FOR INSTRUCTORS:
- Import the STDinSTDout example, use CoolTerm or other terminal app to get STDout.

## Slide 10: Exercise 8
Modify the BlinkTicker example to use LED1, LED2, and LED3 for showing the three least significant bits of an 8-bit counter
Modify the BlinkThreadCallback example so you run two threads that blink different LEDs once per second by waiting for each other