## Slide 1: Fundamentals of IoT Software © 2021 by Luca Mottola is licensed under CC BY-NC 4.0 To view a copy of this license, visit creativecommons.org/licenses/by-nc/4.0/

## Slide 2: Fundamentals of IoT Software BLE with Mbed Luca Mottola luca.mottola@polimi.it (version 0.1)

## Slide 3: Mbed BLE Stack
Efficient BLE implementation called BLE_API
  Hides BLE functionality behind C++ abstractions
Works with SoC and additional hardware modules
Automatically configures the hardware to work at the lowest power consumption

## Slide 4: Inside BLE_API

## Slide 5: Building BLE Beacons
BLE_API provides all functionality for periodic beacon advertisement
Beacon payload and advertising interval remain to be configured
Typically, you may want to advertise
  Company UUID, to identify the bacon manufacturer
  Device UUID, to uniquely identify the beacon
  Major and minor numbers, often used as location information
  Transmission power, for proximity detection

## Slide 6: BLE Beacon Setup
#include <mbed.h>
#include "ble/BLE.h"
#include "ble/services/iBeacon.h"
static iBeacon* ibeaconPtr;
static EventQueue eventQueue(4 * EVENTS_EVENT_SIZE);
void scheduleBleEventsProcessing(BLE::OnEventsToProcessCallbackContext* context) {
BLE &ble = BLE::Instance();
eventQueue.call(Callback<void()>(&ble, &BLE::processEvents));
}
int main()
{
BLE &ble = BLE::Instance();
ble.onEventsToProcess(scheduleBleEventsProcessing);
eventQueue.dispatch_forever();
ble.init(bleInitComplete);
return 0;
}
Use an EventQueue to process events from the BLE stack
Passes the events from the BLE stack to the event queue
Setup and start the event queue, this is alternative to allocating a thread for that
Initialize the BLE stack
Notes: CODE PUBLISHED AT: https://os.mbed.com/users/lmottola/code/IOTSoftware-BLEBeacon/

## Slide 7: BLE Beacon Construction
void bleInitComplete(BLE::InitializationCompleteCallbackContext *params)
{
BLE& ble = params->ble;
ble_error_t error = params->error;
// Check for errors on params->error
static const uint8_t uuid[] = {0xE2, 0x0A, 0x39, 0xF4, 0x73, 0xF5, 0x4B, 0xC4,
0xA1, 0x2F, 0x17, 0xD1, 0xAD, 0x07, 0xA9, 0x61};
uint16_t majorNumber = 1122;
uint16_t minorNumber = 3344;
uint16_t txPower = 0xC8;
ibeaconPtr = new iBeacon(ble, uuid, majorNumber, minorNumber, txPower);
ble.gap().setAdvertisingInterval(1000); ble.gap().startAdvertising();
}
Called once initialization is complete
txPower and compID are optional; using compId default value makes it an iBeacon!
Start advertising every second
The object constructor builds the beacon and registers it with GAP

## Slide 8
Notes: DIRECTIONS FOR INSTRUCTORS:
- Import and run the BLEBeacon, check the output using some smartphone BLE scanner app..

## Slide 9: Exercise 12
Modify the BLE Beacon example so that it advertises
  The current temperature in degree Celsius instead of the minor number
  Only whenever the device is not moving
    Select a simple acceleration threshold to detect movement

## Slide 10: Defining Custom Services
class LEDService {
public:
const static uint16_t LED_SERVICE_UUID = 0xA000;
const static uint16_t LED_STATE_CHARACTERISTIC_UUID = 0xA001;
LEDService(BLEDevice &_ble, bool initialValueForLEDCharacteristic) :
ble(_ble), ledState(LED_STATE_CHARACTERISTIC_UUID, &initialValueForLEDCharacteristic)
{
GattCharacteristic *charTable[] = {&ledState};
GattService ledService(LED_SERVICE_UUID, charTable, 1);
ble.addService(ledService);
}
GattAttribute::Handle_t getValueHandle() const
{
return ledState.getValueHandle();
}
private:
BLEDevice &ble;
ReadWriteGattCharacteristic<bool> ledState;
};
Define UUID for service and characteristic
Initialize class attributes
List of characteristics
Number of characteristics
Notes: CODE PUBLISHE AT: https://os.mbed.com/users/lmottola/code/IOTSoftware-BLELed/

## Slide 11: Advertising Custom Services
void onDataWrittenCallback(const GattWriteCallbackParams *params) {
if ((params->handle == ledServicePtr->getValueHandle()) && (params->len == 1)) {
actuatedLED = *(params->data);
}
}
void bleInitComplete(BLE::InitializationCompleteCallbackContext *params)
{
BLE& ble = params->ble;
ble_error_t error = params->error;
/* Check for errors and BLE instance… */
ble.gattServer().onDataWritten(onDataWrittenCallback);
bool initialValueForLEDCharacteristic = false;
ledServicePtr = new LEDService(ble, initialValueForLEDCharacteristic);
ble.gap().accumulateAdvertisingPayload(GapAdvertisingData::BREDR_NOT_SUPPORTED | GapAdvertisingData::LE_GENERAL_DISCOVERABLE);
ble.gap().accumulateAdvertisingPayload(GapAdvertisingData::COMPLETE_LIST_16BIT_SERVICE_ IDS, (uint8_t *)uuid16_list, sizeof(uuid16_list));
ble.gap().accumulateAdvertisingPayload(GapAdvertisingData::COMPLETE_LOCAL_NAME, (uint8_t *)DEVICE_NAME, sizeof(DEVICE_NAME));
ble.gap().setAdvertisingType(GapAdvertisingParams::ADV_CONNECTABLE_UNDIRECTED);
ble.gap().setAdvertisingInterval(1000);
ble.gap().startAdvertising();
}
Callback to execute when a characteristic is written
…almost boilerplate code.
Check what has been written first!

## Slide 12
Notes: DIRECTIONS FOR INSTRUCTORS:
Build and run the BLE Led example
Change local identifiers
Use a smartphone BLE scanner app to toggle the LED

## Slide 13: Discovery, Connecting, …
Writing a GATT client is generally more complex…
Every operation normally involves setting proper callback(s), triggering the action, and asynchronously processing the results…
  Including connection, service discovery, read/write of characteristics
This typically complicates a program’s control flow!

## Slide 14: Setup and Scanning
void bleInitComplete(BLE::InitializationCompleteCallbackContext *params)
{
BLE& ble = params->ble;
ble_error_t error = params->error;
ble.gap().onDisconnection(disconnectionCallback);
ble.gap().onConnection(connectionCallback);
ble.gattClient().onDataRead(triggerToggledWrite);
ble.gattClient().onDataWrite(triggerRead);
ble.gap().setScanParams(400, 400);
ble.gap().startScan(advertisementCallback);
}
Callbacks to execute when connecting or disconnecting…
Callbacks to execute when a characteristic is read or written on the GATT server!
Scans for 400 ms every 400 ms, that is, continuously; set the callback when receiving an advertisement
Notes: COE PUBLISHED AT: https://os.mbed.com/users/lmottola/code/IOTSoftware-BLELedControl/

## Slide 15: Connecting After Discovery
void advertisementCallback(const Gap::AdvertisementCallbackParams_t *params) {
for (uint8_t i = 0; i < params->advertisingDataLen; ++i) {
const uint8_t record_length = params->advertisingData[i];
const uint8_t type = params->advertisingData[i + 1];
const uint8_t* value = params->advertisingData + i + 2;
const uint8_t value_length = record_length – 1;
if(type == GapAdvertisingData::COMPLETE_LOCAL_NAME) {
if ((value_length == sizeof(PEER_NAME)) && (memcmp(value, PEER_NAME, value_length) == 0)) {
BLE::Instance().gap().connect(params->peerAddr, Gap::ADDR_TYPE_RANDOM_STATIC, NULL, NULL);
break;
}
}
i += record_length;
}
}
Packet parsing
If the peer is PEER_NAME, then connect!
Move to the next record…

## Slide 16: Hooking to a Characteristic
void connectionCallback(const Gap::ConnectionCallbackParams_t *params) {
if (params->role == Gap::CENTRAL) {
BLE &ble = BLE::Instance();
ble.gattClient().onServiceDiscoveryTermination(discoveryTerminationCallback);
ble.gattClient().launchServiceDiscovery(params->handle, serviceDiscoveryCallback, characteristicDiscoveryCallback, 0xa000, 0xa001);
}
}
void characteristicDiscoveryCallback(const DiscoveredCharacteristic *characteristicP) {
if (characteristicP->getUUID().getShortUUID() == 0xa001) { ledCharacteristic = *characteristicP;
triggerLedCharacteristic = true;
}
}
void discoveryTerminationCallback(Gap::Handle_t connectionHandle) {
if (triggerLedCharacteristic) {
triggerLedCharacteristic = false;
eventQueue.call(updateLedCharacteristic);
}
}
Start service discovery after conneting…
Service and characteristic UUID to search for
We found the characteristic within the service, store a pointer to it
Finished discovery, schedule an update to the LED characteristic

## Slide 17: Writing a Characteristic
void updateLedCharacteristic(void) {
if (!BLE::Instance().gattClient().isServiceDiscoveryActive()) {
ledCharacteristic.read();
}
}
void triggerToggledWrite(const GattReadCallbackParams *response) {
if (response->handle == ledCharacteristic.getValueHandle()) {
uint8_t toggledValue = response->data[0] ^ 0x1;
ledCharacteristic.write(1, &toggledValue);
}
}
The EventQueue eventually schedules this…
Toggles the values and writes to the characteristic!

## Slide 18
Notes: DIRECTIONS FOR INSTRUCTORS:
- Build and run the BLELedControl example

## Slide 19: Exercise 13
Form groups of two people
Modify the BLELedControl example so that it toggles the LED on the other board only if you keep the button pressed